## Slide 1: Scaled Measurements of Realistic Counter-DEW Scenarios
EUOREM, London, UK
11 July 2016
Bo Xiao1
Zach Drikas2
Jesus Gil Gil2
T. D. Andreadis2
Tom Antonsen1
Ed Ott1
Steven M. Anlage1
1 University of Maryland, USA
2 US Naval Research Laboratory
Research funded by ONR
ONR/DURIP
AFOSR / AFRL Center of Excellence
Random Coupling Model website:
http://anlage.umd.edu/RCM
Notes: 30 minutes including questions.

## Slide 2
Outline
The Problem: Electromagnetic Interference
Our Approach – A Wave Chaos Statistical Description
The Random Coupling Model (RCM)
Example of the RCM in Practice
New RCM Predictions for Realistic Counter-DEW Scenarios
Scaled measurement system for investigating new RCM predictions
Conclusions

## Slide 3
Electromagnetic Interference and
High-Power Microwave Effects on Electronics
How to defend electronics from electromagnetic interference?
R.F.I. International
Electromagnetic Interference (EMI)
Electromagnetic Compatibility (EMC)

## Slide 4
Electromagnetic Coupling to Enclosures and Circuits A Complicated Problem
Coupling of external radiation to computer chips is a complex process:
  Apertures
  Resonant cavities
  Transmission Lines
  Circuit Elements
System Size >> Wavelength
Chaotic Ray
Trajectories
What can we say about the nature of fields and induced voltages inside such a cavity?
Statistical Description using Wave Chaos!!
Arbitrary Enclosure
(with losses “1/Q”)
Rather than make predictions for a specific configuration,
determine a probability distribution function (PDF) of the
relevant quantities

## Slide 5
Outline
The Problem: Electromagnetic Interference
Our Approach – A Wave Chaos Statistical Description
The Random Coupling Model (RCM)
Example of the RCM in Practice
New RCM Predictions for Realistic Counter-DEW Scenarios
Scaled measurement system for investigating new RCM predictions
Conclusions

## Slide 6
The Difficulty in Making Predictions in Wave Chaotic Systems…
Perturbation Position 1
Perturbation Position 2
(W)
Electromagnetic
Wave Impedance
The extreme sensitivity of the properties of
wave chaotic systems to small perturbations
suggests a statistical approach
The Random Coupling Model incorporates the
underlying chaos into a quantitative statistical
description of the wave properties of real systems
Ray-
Chaotic
Enclosure

## Slide 7
Induced Voltage Statistical Distributions
for Objects in an Arbitrary Enclosure
Arbitrary Enclosure
(with losses “1/Q”)
Port 1
Port 2
Port 3
Port 4
Port 5
Generalized Port
Concept
Port i
Port j
Our approach treats all objects of interest as “ports”
Incident rf energy enters the enclosure through one or more ports
The energy reverberates and is absorbed by one or more ports inside the enclosure
Formulate a quantitative statistical theory of absorbed energy

## Slide 8
Outline
The Problem: Electromagnetic Interference
Our Approach – A Wave Chaos Statistical Description
The Random Coupling Model (RCM)
Example of the RCM in Practice
New RCM Predictions for Realistic Counter-DEW Scenarios
Scaled measurement system for investigating new RCM predictions
Conclusions

## Slide 9
Statistical Model of Impedance (Z) Matrix S. Hemmady, et al., Phys. Rev. Lett. 94, 014102 (2005)
Port 1
Port 2
Other ports
Losses
Port 1
Free-space radiation
Resistance RR(w)
ZR(w) = RR(w) + jXR (w)
RR1(w)
RR2(w)
Statistical Model Impedance
Q -quality factor
Dw2n - mean spectral spacing
Radiation Resistance RRi(w)
win- Guassian Random variables
wn - random spectrum (RMT)
System
parameters
Statistical
parameters
Statistics governed by a single parameter:
L. K. Warne, et al., IEEE Trans. on Anten. and Prop. 51, 978 (2003)
X. Zheng, et al., Electromagnetics 26, 3 (2006); Electromagnetics 26, 37 (2006)
modes n
win wjn
Enclosure

## Slide 10
Outline
The Problem: Electromagnetic Interference
Our Approach – A Wave Chaos Statistical Description
The Random Coupling Model (RCM)
Example of the RCM in Practice
New RCM Predictions for Realistic Counter-DEW Scenarios
Scaled measurement system for investigating new RCM predictions
Conclusions

## Slide 11
Z. B. Drikas, et al., IEEE EMC 56, 1480 (2014)
US Naval Research Laboratory collaboration
Inject microwaves at port 1 and measure induced voltage at port 2
Rotate mode-stirrer and repeat
Plot the PDF of the induced voltage and compare with RCM prediction
But this is at the limit of what we can test in our labs …
Test of the Random Coupling Model: Gigabox Experiment (NRL Collaboration)

## Slide 12
Outline
The Problem: Electromagnetic Interference
Our Approach – A Wave Chaos Statistical Description
The Random Coupling Model (RCM)
Example of the RCM in Practice
New RCM Predictions for Realistic Counter-DEW Scenarios
Scaled measurement system for investigating new RCM predictions
Conclusions

## Slide 13: Coupled Lossy Cavities
RCM predicts the transmission through N cavities coupled through apertures
Experiment requires a chain of Gigaboxes
G. Gradoni, T. M. Antonsen, and E. Ott,
Phys. Rev. E 86, 046204 (2012).
Ability to predict coupled voltage and power along an arbitrary chain of
ray-chaotic cavities/environments/compartments

## Slide 14
Untested RCM Prediction: Induced Voltage Statistics for Enclosures with Mixed
Regular and Chaotic Behavior
Ming Jer Lee, et al., Phys. Rev. E 87, 062906 (2013)
Random Coupling Model still works!

## Slide 15
Outline
The Problem: Electromagnetic Interference
Our Approach – A Wave Chaos Statistical Description
The Random Coupling Model (RCM)
Example of the RCM in Practice
New RCM Predictions for Realistic Counter-DEW Scenarios
Scaled measurement system for investigating new RCM predictions
Conclusions

## Slide 16
Scaling Properties of Maxwell’s Equations for Harmonic EM waves
For example, scaling the GigaBox down by a factor of s = 20 requires:
1 m x 1 m x 1 m Box
5 cm x 5 cm x 5 cm Box
5 GHz measurement
100 GHz measurement
Wall conductivity s
Wall conductivity s*s
Maxwell’s equations are left invariant upon scaling:

## Slide 17
Overview of the Scaled Measurement Project
Test the Random Coupling Model in a set of increasingly complicated
(and realistic) scenarios:
Multiple coupled cavities
Mixed (regular + chaotic) systems
Irradiation through irregular apertures
Evanescent coupling between enclosures
etc.
Perform these tests using scaled-down-in-size models:
To reproduce the same electromagnetic conditions:
Must scale up the frequency to mm-waves
Must scale up the conductivity (cool the metal walls)
ONR/DURIP-funded mm-wave cryogenic measurement system
Validation step: compare to full-scale measurement at NRL

## Slide 18
mm-wave
mm-wave
windows
Teflon lens
Horn antenna
WR10 75-110 GHz
WR3.4 220-330 GHz
Coax ~10 GHz
Coax ~10 GHz
Inside cryostat
Scaled Structure
Reference plane
ONR/DURIP funded experiment setup
Frequency Extender
Frequency Extender

## Slide 19: Experimental Setup
Transmitter
Receiver
mm-wave
Scaled Structure

## Slide 20
Scaled Enclosures (s = 20 and 40)

## Slide 21: Scaled Enclosure Measurement Validation: Compare to NRL Full-Scale Experimental Setup
122.5 cm
66 cm
a = 27.9 cm
a
b
Port 1
Port 2
b = 27.5 cm
Stirrer (Motor Controlled)
44.5 cm
30.5 cm
90˚
2.1 cm
2.5 cm
75 GHz – 110 GHz (s = 20)  3.7 GHz – 5.5 GHz
220 GHz – 330 GHz (s = 40)  5.5 GHz – 8.25 GHz
WR-187 (G-Band)
WR-137 (C-Band)
127.5 cm
25 cm
25 cm
25 cm
c = 25 cm
c
c
c
Zach Drikas, Jesus Gil Gil, T. D. Andreadis @ NRL
We will measure two scaled versions:

## Slide 22
Scaled
Enclosure
(s = 40)
mm-wave
extender
mm-wave
extender
Scaled Enclosure Direct Injection Measurement
3 cm

## Slide 23
Transmission Through s = 40 Cavity
Frequency (GHz)
|S21| (dB)

## Slide 24
First Ensemble Averaged Statistics
(s = 40) Scaled Enclosure (220 – 330 GHz)
9 Realizations
Normalized with Zavg
Room temperature
Best fits to RMT with a = 32.7

## Slide 25: Cryogenic Mode Stirrer
Use cryogenic stepper motor to rotate a magnetic strip below scaled cavity, causing the stirrer panel inside cavity to rotate.
No holes in the cavity walls (no leakage)
Cryogenic stepper motor
Bar Magnet
Stirrer
Scaled enclosure wall

## Slide 26
Multiple Realizations of s = 20 Scaled Enclosure at Cryogenic Temperatures

## Slide 27
Motion of the Perturber (Cu Sheet) Inside
the s = 20 Scaled Enclosure
a = 19
a = 19
Cryogenic Results for the s = 20 Scaled Enclosure
Rotating
Perturber
Statistics with just
9 Realizations

## Slide 28
Top View of Scaled Enclosure Experiment
mm-wave extender
lens
Early Objectives:
Compare Z-statistics results to NRL GigaBox
Measure multiple coupled enclosures and
compare to Gradoni predictions
Aperture illumination of enclosures
Mixed system experiments
cryostat
scaled
enclosure
antenna

## Slide 29: Coupled Cavities Simulation
Circular aperture
Dielectric sphere

## Slide 30
3D Printed Scaled Structures:
Multiple Connected Enclosures
Ports
Scaled
Enclosures
Backplane
with Apertures

## Slide 31
Conclusions
The Random Coupling Model constitutes a comprehensive (statistical) description of the
wave properties of wave-chaotic systems in the short wavelength limit
We believe the RCM is of value to the EMC / EMI community for predicting the statistics
of induced voltages on objects in complex enclosures, for example.
A new measurement system employing scaled structures enables new extensions of RCM:
Multiple connected enclosures
Irradiation through irregular apertures
Systems with mixed (regular and chaotic) properties
Systems with evanescent coupling
RCM Review articles:
G. Gradoni, et al., Wave Motion 51, 606 (2014)
Z. Drikas, et al., IEEE Trans. EMC 56, 1480 (2014)
Research funded by ONR
ONR/DURIP
AFOSR / AFRL Center of Excellence
anlage@umd.edu
http://anlage.umd.edu/RCM

## Slide 32
The Maryland Wave Chaos Group
Tom Antonsen
Steve Anlage
Ed Ott
Jen-Hao Yeh
LPS
James Hart
Lincoln Labs
Biniyam Taddese
FDA
Also:
Undergraduate Students
Eliot Bradshaw
John Abrahams
Gemstone Team TESLA
Post-Docs
Gabriele Gradoni
Mathew Frazier
NRL Collaborators: Tim Andreadis, Lou Pecora, Hai Tran, Sun Hong, Zach Drikas, Jesus Gil Gil
Funding: ONR, AFOSR, DURIP
John Rodgers
NRL, Naval Academy,
UMD
Ming-Jer Lee
World Bank
Trystan Koch
Faculty
Graduate Students (current + former)
Mark Herrera
Heron Systems
Bo Xiao
Bisrat Addissie

## Slide 34: Scaling
Size scale down
  Wavelength ,
  Skin depth ,
  Conductivity
Frequency scaling:
  5 GHz -> 100 GHz (s=20)
200 GHz (s=40)
Conductivity Scaling:
  Copper in low temperature
s=20, 40

## Slide 35
Im
PDF
PDF
Im
PDF
PDF
Normalized real(Z11)
Normalized imag(Z11)
Normalized real(Z21)
Normalized imag(Z21)
220 ~ 330 GHz

## Slide 36
VDI mm-wave
extenders:
75 – 110 GHz;
110 – 220 GHz;
220 – 330 GHz
Keysight N5242A
4-port Vector Network
Analyzer
BlueFors Dry Dilution
Refrigerator, 50-cm-
diameter MXC plate
DUT

## Slide 37
Untested Prediction #2 Induced Voltage Statistics for Irradiation Through an
Irregular Aperture
Treat both the aperture and the enclosure statistically
Relevant variables:
Loss in the enclosure
Scaling prediction involving size of aperture and enclosure losses
….

## Slide 38
It makes no sense to talk about
“diverging trajectories” for waves
1) Waves do not have trajectories
Wave Chaos?
2) Linear wave systems can’t be chaotic
3) However in the semiclassical limit, you can think about rays
Wave Chaos concerns solutions of linear wave equations which,
in the semiclassical limit, can be described by chaotic ray trajectories
In the ray-limit
it is possible to define chaos
“ray chaos”
Maxwell’s equations, Schrödinger’s equation are linear

## Slide 39: Transmission Through Cavity
Transmission ≈ -20 dB
Scaled copper cavity in room temperature
NRL full-scale experiment
Next step: Cool the scaled cavity to
reduce a to that seen in the NRL experiment
  Pin = 1 W
  Zload = 50 W

## Slide 40
Untested Prediction #4 Statistics of tunneling (coupling)
between enclosures through apertures that are below cutoff
Relevant variables:
Do regular enclosures show stronger coupling? Should we make enclosure ray-chaotic?
We need reasonably-sized waveguides that are below cutoff
….
Fluctuations in the transfer (tunneling) rate are stronger for regular vs. chaotic enclosures