## Slide 1
Overview of EM Guided Waves
and Microwave Measurements
Steven Anlage
http://www.cnam.umd.edu/anlage/AnlageMicrowaveMeasurements.htm

## Slide 2
Guided Waves
Transmission Lines
Characteristic Impedance
Waveguides
Network Analysis
Linear vs. Nonlinear Properties
Spectrum Analysis
Resonator Measurements
Outline

## Slide 3
Electrical Signals at Low and High Frequencies

## Slide 4
Transmission Lines
Transmission lines carry microwave signals from one point to another
They are important because the wavelength is much smaller than the length of typical T-lines
used in the lab
You have to look at them as distributed circuits, rather than lumped circuits
The wave equations
V

## Slide 5
Transmission Lines
Wave Speed
Take the ratio of the voltage and current waves
at any given point in the transmission line:
= Z0
The characteristic impedance Z0 of the T-line
Reflections from a terminated transmission line
ZL
Z0
Reflection
coefficient
Some interesting special cases:
Open Circuit ZL = ∞, G = 1 ei0
Short Circuit ZL = 0, G = 1 eip
Perfect Load ZL = Z0, G = 0 ei?
These are used in error correction measurements to characterize non-ideal T-lines

## Slide 6
Transmission Lines and Their Characteristic Impedances

## Slide 7
The power absorbed in a termination is:
Transmission Lines, continued
Model of a realistic transmission line including loss
Traveling
Wave
solutions
with
Shunt
Conductance

## Slide 8
How Much Power Reaches the Load?

## Slide 9
The Need for Care with SMA Connectors

## Slide 10
Microwave Connectors
Connector Name | Bandwidth (GHz) | “Compatible” with | Found in
1 mm | 110 |  | 
V (1.85 mm) | 60 | 2.4 mm | Corbino expt.
2.4 mm | 60 | V | PNA
K (2.92 mm) | 40 | 3.5 mm*, SMA* | BlueFors fridge
3.5 mm | 26.5 | K, SMA* | PNA
SMA | 18 or 25 | 3.5 mm, K | All over…
* Means “mates with damage”
See https://www.microwaves101.com/encyclopedias/microwave-connectors#overview

## Slide 11
Waveguides
Rectangular metallic waveguide
H

## Slide 12
Network Analysis
Assumes linearity!

## Slide 13
Quantum Scattering in One Dimension
Griffiths 3rd Edition, problem 2.53
https://www.physics.umd.edu/courses/Phys402/AnlageFall22/Quantum%20Scattering%20in%20One%20and%20Three%20Dimensions.pdf

## Slide 14
Scattering From a Finite Potential Well in 1D Quantum Mechanics

## Slide 15
https://www.open.edu/openlearn/science-maths-technology/science/physics-and-astronomy/scattering-and-tunnelling/content-section-3.5
Parameters used:
m = mass of electron
V0 = 8.6 eV
2a = 1 nm
Transmission Probability vs. Incident Particle Energy
Perfect transmission resonances at
which corresponds to:
Ramsauer-Townsend
Effect

## Slide 16
N-Port Description of an Arbitrary Enclosure
N – Port
System
N Ports
Voltages and Currents,
Incoming and Outgoing Waves
Z matrix
S matrix
V1 , I1
VN , IN
Complicated Functions of frequency
Detail Specific (Non-Universal)

## Slide 17
Common Microwave Devices and How They Work
Microwave devices and measurements boil down to simply separating left-going and right-going waves on a transmission line
Circulator
Non-idealities:
Reflection coefficient
Finite directivity (e.g. )
Can be nonlinear at high power

## Slide 18
Common Microwave Devices and How They Work
Microwave devices and measurements boil down to simply separating left-going and right-going waves on a transmission line
Isolator = Circulator + matched load on port 3
Non-idealities:
Reflection coefficient
Finite directivity (e.g. )
Can be nonlinear at high power

## Slide 19
Common Microwave Devices and How They Work
Directional Coupler
Most of the signal goes through
A small amount (e.g. -10 dB, or -20 dB) of the right-going wave is sampled off for measurement
The sampled reflected (left-going) wave is absorbed

## Slide 20
Divider / Splitter / Combiner / Tee
Common Microwave Devices and How They Work

## Slide 21
Bias tee – Combines / Separates microwave and DC / low-frequency signals
Common Microwave Devices and How They Work
Bias tees are built into the network analyzers
The DC/low-frequency connection is
on the back-panel

## Slide 22
Linear vs. Nonlinear Behavior

## Slide 23
Network vs. Spectrum Analysis

## Slide 24
Resonator Measurements
Sample
Microwave
Resonator
Cavity
Perturbation
input
output
Traditional Electrodynamics Measurements
Hrf
rf currents
inhomogeneities
~ microwave
wavelength
l
These measurements
average the properties
over the entire sample
frequency
transmission
f0
df
f0’
df’
Df = f0’ – f0  D(Stored Energy)
D(1/2Q)  D(Dissipated Energy)
Quality Factor
Q = Estored/Edissip.
Q = f0 / df
T1
T2
B
sample

## Slide 25
Electric and Magnetic Perturbations
Sample
E
e1 - i e2
s, r/t
Rs + i Xs
Varying capacitance (e1) and
inductance (m1) change the stored
energy and resonant frequency Df
Df = f0’ – f0  D(Stored Energy)
D(1/2Q)  D(Dissipated Energy)
Varying sample losses (r/t,
tand = e2/e1, m2) change the quality
factor (Q) of the microscope
Magnetic Field Pert.
m1 + i m2
s, r/t
Rs + i Xs
Sample
E
Electric Field Pert.
B
B
Sphere in
electric field
Pin in
electric field
sphere

## Slide 27
The Variable-Spacing Parallel Plate Resonator
Principle of Operation: Measure the resonant frequency, f0, and the
quality factor, Q, of the VSPPR versus the continuously variable
thickness of the dielectric spacer (s), and to fit them to theoretical forms
in order to extract the absolute values of l and Rs.
Vary s
s: contact –
~ 100 mm
in steps of
10 nm to 1 mm
The measurements are performed at a fixed temperature
In our experiments L, w ~ 1 cm

## Slide 28
The VSPPR Experiment
Films held and aligned by two sets
of perpendicular sapphire pins
Dielectric spacer thickness (s)
measured with capacitance meter

## Slide 29
VSPPR: Theory of Operation
V. V. Talanov, et al., Rev. Sci. Instrum. 71, 2136 (2000)
US Patent # 6,366,096
Superconducting samples
Quality Factor
fringe
effect
SC Trans.
line resonator
Resonant Frequency
Assumes: 2 identical and uniform films, local electrodynamics, Rs(f) ~ f2
f* is a reference frequency

## Slide 30
High-Tc Superconducting Thin Films at 77 K
l fit: 257 ± 25 nm
Rs fit: 200 ± 20 mW @ f* = 10 GHz
L = 9.98 mm, w = 9.01 mm, film thickness d = 760 ± 30 nm, Tc = 92.4 K
Mutual Inductance Measurements
(l1+l2)/2 = 300 ± 15 nm